## Slide 1: Writing a Testbench
Nihar Shah
Abhinav Sridhar

## Slide 2: Testbench
Used for testing of design
Testing takes more than 60% of time in the process of coming up with a design

## Slide 3: Testbench
It has entity without any ports is defined first
It has 2 or more concurrent statements
One of the concurrent statements is necessarily an instantiation of the main design as a component
Common practice is to name this instance as uut (unit under test) or dut (design under test)
The other statement(s) may be processes, feeding inputs one by one to the system or just varying a set of inputs

## Slide 5: Additional Points
Although it is recommended for smaller designs, a testbench may not consider every single test case, only corner cases may be enough for some designs
Eg. For the design of an 32 bit adder, there are 2^65 possible input combinations (considering input carry as well)
In case it takes 1 ns for execution of each case, it will take more than 28000 years to test every possible case

## Slide 6: Exercise for Practice
Design a similar testbench for the 16:1 Mux and 1 bit full adder you have designed
Consider all 8 test cases for the full adder and simulate on Quartus/Modelsim